## Slide 1
VLANs
Virtual Local Area Networks
Cybersecurity AEC Program
What they are · How they are used · Tagging explained
1 / 15

## Slide 2
The Problem: Flat Networks
What happens when there is no segmentation?
A company with four departments — Sales, HR, Engineering, Research — all on daisy-chained switches with a single router:
1
Broadcast Flooding
A single ARP request from Sales reaches every device on the entire network, wasting bandwidth across all departments.
Every broadcast hits every host.
2
Single Point of Failure
If one middle switch dies, every department behind it is completely cut off from the network and Internet.
One failure isolates entire groups.
3
Zero Logical Separation
Any user can sniff traffic from any other department. No boundary between sensitive HR data and Sales.
No security between departments.
KEY TAKEAWAY A flat network has no segmentation — broadcasts reach everyone, failures cascade, and there is no isolation between departments.
2 / 15

## Slide 3
What Is a VLAN? (1/2)
Definition & the Hotel Analogy
VLAN = Virtual Local Area Network
A VLAN takes one physical switch and divides it into multiple independent, logical switches — each with its own isolated broadcast domain.
The Hotel Analogy
Imagine a 10-floor hotel. Without VLANs, every guest shares the same hallways and noise. With VLANs, invisible walls create separate zones:
Floors | Zone | Access
1 – 3 | Business Zone | Business guests only
4 – 6 | Family Zone | Families only
7 – 10 | VIP Zone | VIP guests only
Physical vs. Logical
Same physical building
Completely separate logical spaces
Guests in one zone cannot access another
A VLAN does exactly this for a network switch.
KEY TAKEAWAY A VLAN is a virtual broadcast domain — it segments one physical switch into multiple isolated logical networks, no extra hardware required.
3 / 15

## Slide 4
What Is a VLAN? (2/2)
Four fundamental properties
1
Each VLAN = One Broadcast Domain
A broadcast in VLAN 10 stays in VLAN 10. Period. Other VLANs never see it.
2
Location-Independent
Users don't need to be physically next to each other. An engineer on Floor 1 and Floor 3 can share the same VLAN.
3
Inter-VLAN = Layer 3 Required
Communication between VLANs requires a router or multilayer switch. Without one, VLANs are completely isolated.
4
Default: All Ports in VLAN 1
On Cisco switches, every port starts assigned to VLAN 1. You must manually assign ports to other VLANs.
KEY TAKEAWAY Communication between VLANs only happens through a Layer 3 device (router). Without routing, VLANs are like separate physical networks.
4 / 15

## Slide 5
VLANs in Cybersecurity (1/2)
Three critical security functions
1. Segmentation & Lateral Movement Prevention
▸ An attacker who compromises a workstation in VLAN 30 (Sales) is trapped inside that VLAN
▸ Cannot directly reach servers in VLAN 10 or management interfaces in VLAN 99
▸ Limits lateral movement — one of the most dangerous phases of a cyberattack
▸ MITRE ATT&CK: Lateral Movement (TA0008)
2. Access Control Enforcement
▸ VLANs + ACLs or firewall rules at Layer 3 control who communicates with whom
▸ Example: Guest Wi-Fi VLAN reaches Internet but has zero access to internal file servers
3. Regulatory Compliance
▸ PCI-DSS requires cardholder data environments to be segmented
▸ HIPAA, SOX, and NIST 800-171 all recommend or mandate network segmentation
▸ VLANs are a primary tool to achieve and demonstrate compliance
KEY TAKEAWAY VLANs limit lateral movement, enforce access boundaries, and satisfy compliance mandates like PCI-DSS, HIPAA, and NIST 800-171.
5 / 15

## Slide 6
VLANs in Cybersecurity (2/2)
Limitations — VLANs are NOT firewalls
IMPORTANT CAVEAT
VLANs operate at Layer 2 only — they are not a substitute for a firewall
Security professionals must know how to build these controls AND how to break them
VLAN Hopping: Double-Tagging
Attacker crafts a frame with two 802.1Q tags. The outer tag matches the native VLAN, the inner tag targets a victim VLAN. The first switch strips the outer tag and forwards the inner-tagged frame to the victim VLAN.
VLAN Hopping: Switch Spoofing
Attacker configures their NIC to negotiate a trunk with the switch using DTP (Dynamic Trunking Protocol). If successful, the attacker's port becomes a trunk and can access all VLANs.
Mitigations
▸ Change native VLAN to an unused VLAN
▸ Disable DTP on all access ports (switchport nonegotiate)
▸ Explicitly configure access ports — never leave them in dynamic mode
▸ Prune unused VLANs from trunks
6 / 15

## Slide 7
The Tagging Problem
Why standard Ethernet frames aren't enough
Standard Ethernet Frame — No VLAN field exists:
Dest MAC
Source MAC
EtherType
Payload
FCS
The Problem:
Two switches share traffic from multiple VLANs over a single cable (trunk)
When Switch B receives a frame, it has no way to know if it came from VLAN 10 or VLAN 20
The standard Ethernet frame has no VLAN identification field whatsoever
The Solution: Trunk Links + a Tagging Protocol
Protocol | Standard | Support
802.1Q | IEEE open standard | All major vendors — industry standard
ISL | Cisco proprietary (legacy) | Cisco only — being phased out
KEY TAKEAWAY Standard Ethernet frames carry no VLAN information. Trunk links use 802.1Q tagging to label each frame with its VLAN identity.
7 / 15

## Slide 8
802.1Q Tag — Anatomy
A 4-byte tag inserted into the Ethernet frame
802.1Q Tagged Frame:
Dest MAC
Source MAC
802.1Q TAG
EtherType
Payload
FCS
Inside the 802.1Q Tag (4 bytes / 32 bits):
Field | Size | Purpose
TPID (Tag Protocol ID) | 16 bits | Fixed value 0x8100 — identifies frame as 802.1Q tagged
PCP (Priority Code Point) | 3 bits | QoS priority level (0–7); e.g., VoIP = priority 5
DEI (Drop Eligible) | 1 bit | Marks frame as eligible for dropping under congestion
VID (VLAN Identifier) | 12 bits | The VLAN number — range 0–4095, usable: 1–4094
Key Numbers to Remember:
4 bytes
Total tag size
12 bits → 4,094
Usable VLANs
0x8100
EtherType identifier
8 / 15

## Slide 9
How Tagging Works — Step by Step
Computer A (VLAN 10, Switch A) → Computer B (VLAN 10, Switch B)
Step | Action | Frame State
1 | Computer A sends a normal Ethernet frame into Switch A's access port (VLAN 10) | Untagged
2 | Switch A associates the frame with VLAN 10 based on port assignment | —
3 | Switch A inserts the 802.1Q tag (VID=10) and sends it out the trunk port | Tagged
4 | Switch B receives the frame on its trunk port and reads the tag: VLAN 10 | Tagged
5 | Switch B removes the tag and delivers the clean frame to Computer B (VLAN 10) | Untagged
Two Essential Rules:
Rule 1: End devices never see the tag
Tagging/untagging happens entirely on trunk links between switches
Rule 2: Access ports = always untagged
The switch handles VLAN identification internally based on port assignment
KEY TAKEAWAY Switches add the 802.1Q tag when sending onto a trunk and strip it when delivering to an access port. Tagging is transparent to hosts.
9 / 15

## Slide 10
The Native VLAN
The exception to the tagging rule
The native VLAN is the one VLAN on a trunk whose frames are sent WITHOUT an 802.1Q tag.
Property | Detail
Default native VLAN | VLAN 1
Behavior on trunk | Native VLAN frames cross the trunk untagged
Receiving switch | Untagged frames on a trunk → assumed native VLAN
Critical requirement | Native VLAN must match on both sides of the trunk
What travels here? | CDP, STP BPDUs, VTP, and non-802.1Q-aware devices
Security: Double-Tagging Attack
▸ Attacker sends frame with two 802.1Q tags
▸ Outer tag = native VLAN (gets stripped)
▸ Inner tag = victim VLAN (gets forwarded)
▸ Result: frame reaches a VLAN it shouldn't
Best Practices:
▸ Change native VLAN from VLAN 1 to an unused VLAN
▸ Match native VLAN on both ends of every trunk
▸ Tag the native VLAN explicitly (Cisco: vlan dot1q tag native)
KEY TAKEAWAY The native VLAN is untagged on trunks — a VLAN hopping vector. Always change it from default, ensure it matches, and consider tagging it.
10 / 15

## Slide 11
Port Types at a Glance
Access port vs. Trunk port
ACCESS PORT
Belongs to
One single VLAN
Connected to
End devices (PCs, printers, phones)
Tagging
None — frames always untagged
VLAN assignment
Configured per-port
Switch behavior
Associates all incoming frames with the configured VLAN
TRUNK PORT
Belongs to
Carries multiple VLANs
Connected to
Other switches or routers
Tagging
802.1Q on all VLANs (except native)
VLAN assignment
Allowed VLAN list configurable
Switch behavior
Reads 802.1Q tag to determine VLAN; untagged → native
KEY TAKEAWAY Access ports = single VLAN, untagged, for end devices. Trunk ports = multiple VLANs, 802.1Q tagged, for switch-to-switch links.
11 / 15

## Slide 12
InterVLAN Routing
Bridging the gap between isolated VLANs
VLANs are isolated by design — a device in VLAN 10 cannot reach VLAN 20 at Layer 2. A Layer 3 device must route between them.
1
Router on a Stick
Single router with sub-interfaces, one per VLAN, connected via 802.1Q trunk to the switch.
Best for: Small networks, labs
2
SVI (Switch Virtual Interface)
Multilayer (L3) switch creates virtual interfaces per VLAN and routes internally — fast, no extra hardware.
Best for: Enterprise networks
3
Routed Port
Switch port configured as a Layer 3 interface (no VLAN) for point-to-point routing.
Best for: Distribution / core uplinks
Security: Every inter-VLAN routing point is a policy enforcement point — apply ACLs or firewall rules to control which VLANs communicate.
KEY TAKEAWAY VLANs isolate at Layer 2; Layer 3 routing is required for inter-VLAN communication. Each routing point is an opportunity for security policy enforcement.
12 / 15

## Slide 13
Troubleshooting VLANs & Trunks
Common issues and verification
VLAN Problems
Symptom | Likely Cause
Same-VLAN hosts can't communicate | Ports in different VLANs
No connectivity after VLAN change | VLAN doesn't exist on switch
Traffic blocked unexpectedly | VACL (VLAN Access List) applied
Trunk Problems
Symptom | Likely Cause
Trunk not forming | Encapsulation mismatch
Some VLANs not passing | Not in allowed list
Intermittent connectivity | Native VLAN mismatch
Wrong port mode | DTP negotiation conflict
Essential Verification Commands (Cisco IOS)
Command | What It Shows
show vlan brief | VLAN list and port assignments
show interfaces trunk | Trunk status, encapsulation, native VLAN, allowed VLANs
show interfaces switchport | Detailed port mode and VLAN information
KEY TAKEAWAY Most issues: wrong VLAN assignment, VLAN not created, encapsulation mismatch, native VLAN mismatch, or VLAN missing from trunk allowed list.
13 / 15

## Slide 14
Summary — The Big Picture
VLANs segment a physical switch into isolated virtual broadcast domains, enabling security, performance, and compliance.
1
VLAN = Virtual Broadcast Domain
One physical switch → multiple isolated logical networks
2
802.1Q = The Tagging Protocol
A 4-byte tag with 12-bit VLAN ID inserted on trunk links
3
VLANs = A Cybersecurity Control
Limits lateral movement, enforces access, meets PCI-DSS
What Connects Forward:
This Lesson | Leads To
VLAN isolation | InterVLAN routing (Router on a Stick, SVIs)
802.1Q tagging | VLAN hopping attacks & mitigation
Native VLAN | Double-tagging attack lab
Access vs. trunk ports | Port security & 802.1X authentication
Network segmentation | Zero Trust Architecture
14 / 15

## Slide 15
Challenge Question
?
If VLANs isolate networks at Layer 2, what device or mechanism do we need to allow a host in VLAN 10 to communicate with a host in VLAN 20 — and what new security risks does that introduce?
Hint: The answer connects networking fundamentals to firewall policy, ACL design, and the principle of least privilege.
Think about this before next class!
15 / 15